## Slide 1
Penning Trap Mass Measurements at TITAN
April 19, 2017
American University Physics Seminar
D. Lascar | Postdoctoral Fellow | TRIUMF

## Slide 2: Precision v. Accuracy
Not Accurate
Precise
x
x
x
x
x
x
x
x
x
x
Accurate
Precise
x
x
x
x
x
x
x
x
x
Accurate
Not Precise
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Not Accurate
Not Precise
x
x

## Slide 3: Why measure masses?
Molar mass
  35.453 ± 0.002 g/mol 35.453(2) g/mol
  particles/mol
  If you measure out 35.453 g precisely
    6.02214(34) x 1023 atoms
  Does it matter?
    Depends on the application
Chlorine
35.453
Notes: Molar mass uncertainty is all that matters

## Slide 4: Why measure masses?
 | Mass (AMU) | m - M(180Hf) (AMU) | 
180Hf | 179.9466 | -- | --
179HfH | 179.9538 | 0.0071 | 3.94 x 10-5
C6H12O6 | 180.0648 | 0.1168 | 6.49 x 10-4
C9H8O4 | 180.0432 | 0.0957 | 5.32 x 10-4
C10H12O3 | 180.0800 | 0.1321 | 7.34 x 10-4
C7H7F3O2 | 180.0406 | 0.0933 | 5.18 x 10-4
 | Mass (AMU) | m - M(180Hf) (AMU) | 
180Hf | 179.9466 | -- | --
179HfH | 179.9538 | 0.0071 | 3.94 x 10-5
C6H12O6 | 180.0648 | 0.1168 | 6.49 x 10-4
C9H8O4 | 180.0432 | 0.0957 | 5.32 x 10-4
C10H12O3 | 180.0800 | 0.1321 | 7.34 x 10-4
C7H7F3O2 | 180.0406 | 0.0933 | 5.18 x 10-4

## Slide 5: What do masses tell us?
Nuclear Masses of Rare Isotopes:
  Magic numbers of exotic nuclei (new shell closures)
  R-process waiting points
  Inform theory
  CKM matrix
Notes: Masses used in almost every subfield of physics
Only difference is the precision required
For astrophysics that’s 10 keV/c2
For QED that’s 1eV/c2

## Slide 6: Nuclear mass models are…
Model difference (MeV)
Notes: Clearly we need the masses of nuclei far from stability.
In the region of known masses, models are quite good but not terribly useful -> Why use a model when you have the data?

## Slide 7: Nuclear mass models are…insufficient
Model difference (MeV)
Notes: Further from stability, where the explosive astrophysical processes occur, there’s much more disagreement.
For the most part, that’s the area where I study. WHY?

## Slide 8: Explosive nucleosynthesis
Courtesy of J. Blondin NCSU
http://wonka.physics.ncsu.edu/~blondin/AAS/
C. Ott et al ApJ 768, 115 (2013)
Type-I X-ray burst
Type-II (CC) SN
Neutron star merger
S. Rosswog et al MNRAS 430 4 (2013)

## Slide 9: Nuclear Astrophysics
Big Bang
  1H, 2H, 3He, 4He, 6Li, 7Li
Cosmic Ray Spallation (interstellar medium)
  Many elements, including most Li, Be, B
Stellar Burning
  Up to 56Fe
p Process (core-collapse supernovae)
  Some heavy elements
rp/νp Process (x-ray bursts)
s Process (AGB stars)
  Heavy elements up to A=208 (half of all heavy nuclei)
r Process (??)
  Heavy elements A>56 (the other half)
Notes: Triple- -> 8Be + = 12C
Question 3:
  How were the heavy elements from iron to uranium made?
  Feb. 1, 2002
Triple-𝛼 -> 𝛼+𝛼= 8Be + 𝛼 = 12C
Question 3:
  How were the heavy elements from iron to uranium made?
  Feb. 1, 2002

## Slide 10: The astrophysical r-process
Temperatures are very high (T~109K)
Neutron densities are very high (nn > 1020 cm-3)
(n,g) rate is high ( < 1 ms/capture )
As region of low neutron separation energy (Sn) reached (n,g) ↔ (g,n) equilibrium achieved
[A. Champagne, RIA Summer School ‘06]
Notes: As Sn drops, the number of available photons with enough energy knock out a neutron increase.

## Slide 11: The astrophysical r-process
Temperatures are very high (T~109K)
Neutron densities are very high (nn > 1020 cm-3)
(n,g) rate is high ( < 1 ms/capture )
As region of low neutron separation energy (Sn) reached (n,g) <-> (g,n) equilibrium achieved
Equilibrium point defined by Saha Equation
Z
N
…
Neutron density
Temperature
Neutron separation energy
Notes: The left size is the ratio of relative abundance between two adjacent isotopes.

## Slide 12: So we wait for a b-decay
The Sn where equilibrium occurs depends only on T and nn
[A. Champagne, RIA Summer School 06]
Notes: Walk through the process. Start with Stability and the s-process then move towards the r-process.
Note the path density at the closed shells.

## Slide 13: Neutron separation energy and mass

## Slide 14: How to measure masses?
Dipole mass spectrometry
Charged particle in a uniform magnetic field
(Magnetic force)
(F is a centripetal force)
Magnetic Rigidity ():
Best
+
+
Radius of curvature

## Slide 15: How to measure masses?
Time of flight mass spectrometry
Measure the time that an ion at known energy will travel a known distance.
Can be linear
  Space limitation
Storage rings better
  Distance unlimited
Best precision:

## Slide 16: We can do better than
Actually we need
  For nuclear astrophysics minimum
  For fundamental symmetries: minimum
What is the physical quantity that we can measure to the highest precision?

## Slide 17: Time
Time is the physical quantity we can measure most precisely
For this clock:
We can do better than
When making a precision measurement, the goal is to measure time (frequency)
For next class:
How can you relate a time (frequency) measurement to mass?
Notes: 1 second in 3 billion years

## Slide 18: How do you relate time to mass?
Put it in a magnetic field
  Long enough that it can complete multiple orbits.
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
+

## Slide 19: How do you relate time to mass?
Put it in a magnetic field
  Long enough that it can complete multiple orbits.
Can’t come in perpendicularly
Radius is a function of initial energy but you’ll never do better than a semicircle
How to get a full orbit?
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
+

## Slide 20: How do you relate time to mass?
Put it back in a magnetic field
  This time for longer.
  Long enough that it can complete multiple orbits.
Send it along a uniform -field
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
+
Any perpendicular component will induce an oscillation
+

## Slide 21: What about the axial direction?
The ion will keep moving along.
Doesn’t give us much time to study it.
What should we do?
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
+
+

## Slide 22: What about the axial direction?
Create a potential well.
All you need are a few electrodes
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
+
+

## Slide 23: A Penning Trap
Electrodes create an axial quadrupole trapping potential
  The potential repels in the radial direction but B takes care of that
Quadrupole potential created by making the electrodes conform to 2 hyperboloids of revolution.
Notes:   Point out that potential repels in the radial direction. It’s important later next slide.
  Plus correction electrodes to account for finite extent of the hyperboloids and for the apertures.
Explain what a quadrupole potential is.
  X2 potential.
  Simple harmonic oscillator
  We know how to solve it

## Slide 24: Trapping ions
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
+
+
+

## Slide 25: Trapping ions
Ions are trapped in 3 dimensions
Now you can study them
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
+
+

## Slide 26: Penning trap
Motion of ions well understood:
Three Eigenmotions can be coupled using RF
Allows us to manipulate motion:
transfer from one motion into the other
Cyclotron frequency:
Superposition of
strong magnetic field
weak electrostatic quadrupole field
kHz
MHz
Notes: Time is the physical quantity we can measure most precisely.
Talk about decoupling of eigenmotions
  weakly mass dependent
  strongly mass dependent
Talk about decoupling of eigenmotions
𝜈_− weakly mass dependent
𝜈_+ strongly mass dependent

## Slide 27: Dipole and quadrupole excitations
DIPOLE EXCITATIONS
QUADRUPOLE EXCITATIONS

## Slide 28: Energy Conversion
Magnetic field lines outside the Penning trap
Ions from the Penning trap
Orbital
Energy
Linear
Energy
TOF
Detection
c Excitation
Notes: We measure the energy by measuring the time of flight from the PT to a channeltron detector above the trap and outside of the magnetic field.
We need to know how much energy we’ve put into the system so we need to convert the orbital energy to linear energy.

## Slide 29: Sample ToF spectrum
Unknown:
Time of Flight (arb units)
Slide courtesy of J. Van Schelt
Frequency (kHz)
133Cs
fc=663,104.706(3) Hz (560 eV/c2)
Notes: 133Cs was chosen because it is close in mass to what we were measuring and because it’s precision is dm/m = 1.7 E-10.
Click early: trf is the amount of time that the excitation has been applied for

## Slide 30: Sample ToF Spectrum
Unknown:
fc=663,104.706(3) Hz (560 eV/c2)
Time of Flight (arb units)
Slide courtesy of J. Van Schelt
Frequency (kHz)
For 1 s excitation, Width ~1Hz = Δν
Δm ≈ 200 keV/c2
133Cs
Notes: 133Cs was chosen because it is close in mass to what we were measuring and because it’s precision is dm/m = 1.7 E-10.
Click early: trf is the amount of time that the excitation has been applied for

## Slide 33
Cyclotron
ISAC-I
ISAC-II

## Slide 34: ISAC-I
TITAN

## Slide 37: The TITAN facility
RFQ: Accumulation, cooling, and bunching
EBIT: ms charge breeding
BNG: fast m/q selection
MPET: mass measurement via cyclotron frequency determination
Notes: Going to a higher charge state is particularly important for TITAN because of…next slide

## Slide 38: Linear Paul Trap
The TITAN RFQ
Necessary ingredients
250 kHz to 1 MHz RF along the electrodes
Axial DC gradient
Buffer gas cooling on the order of a few ms
Radial trajectory of 133Cs in 2.5 x 10-2 mbar
Viscous drag model calculation
(mm)
10 mm
Similar to TITAN RFQ
NIMA 676 (2012) 32
Slide courtesy of T. Brunner

## Slide 39: Improving Precision
What can we do to improve mass precision?
Get a stronger magnet
Measure for longer
Get more statistics
Measure a smaller mass
Measure higher charge state
Expensive
What if the species is short lived?
Not normally an option

## Slide 40: The TITAN facility
RFQ: Accumulation, cooling, and bunching
EBIT: ms charge breeding
BNG: fast m/q selection
MPET: mass measurement via cyclotron frequency determination
Notes: Going to a higher charge state is particularly important for TITAN because of…next slide

## Slide 41: Electron Beam Ion Trap
Superconducting magnet, Helmholtz configuration, ≤ 6 T
Design limits on electron beam 70 keV & 5 A
7 radial ports with recessed Be windows
A. Lapierre et al., NIMA 624 (2010) 54
Sikler lens
cathode
electron gun
500 mA achieved
Notes: 6 T

## Slide 42: Short Measurement Times
TITAN specializes in short measurement cycles.
Measure masses of some of the shortest lived nuclides ever.
  31Na (t1/2 = 17 ms)
  32Na (t1/2 = 13 ms)
  11Li (t1/2 = 9 ms)
nc = qe/m ∙ B/2p
31Na+
T1/2 = 17 ms
32Na+
T1/2 = 13 ms
Notes: Tests have shown that we can go get to high precision with a 5ms excitation time
keV. keV
Tests have shown that we can go get to high precision with a 5ms excitation time
𝛿_"Na" =30 keV. 𝛿_"Li" =64 keV

## Slide 43: S1466 & S1502
10 days
Some of the cleanest beam from IGLIS
Measured masses of 18 states:
  125,125m,126,127,127mCd
  125,125m,126,126m,127,127mIn 128,128m,129,129mIn 130,130m1,130m2In
PRL & PRC in prep
127,mCd
Preliminary
127Cd
127mCd
Preliminary
Notes: In all cases where we observed isomers, we observed the g.s. in the same spectrum

## Slide 44
1.707(15) MeV isomer offscreen
Conflated States
Notes: CPT measured 130In (and reported conflated states) but is seems clear that the conflated states reported wasn’t the ground state.
Still, TITAN is doing the same because NUBASE reports a 50 keV isomer and we didn’t see it either

## Slide 45: The Atomic Mass Evaluation

## Slide 46: July 2016: S1466 & S1502
10 days
Some of the cleanest beam from IGLIS
Measured masses of 18 states:
  125,125m,126,127,127mCd
  125,125m,126,126m,127,127mIn 128,128m,129,129mIn 130,130m1,130m2In
Will yield 2 pubs. min.
Misidentified isomer
Notes: Good agreement in most cases.
Note that this is from the 2012 AME
It looks like JYFLTRAP misidentified the g.s. and measured the isomer so the isomer is what is listed in the AME

## Slide 47: JYFLTRAP Data

## Slide 48: Mass Measurements
Analysis of July Cd data is complete
  Values are included in the 2016AME (just published)
Able to resolve more isomers than ever before
PRL should be submitted before the end of the month
Notes: Looked at the isomers with respect to calculations from the NuShellX shell model code using the jj45 interaction which is the only one available for this mass region.

## Slide 49
Thank you!
Merci!
Giessen
C. Andreoiu, J.C. Bale, B.R. Barquest, T. Brunner, U. Chowdhury, A. Finlay, D. Frekers, A.T. Gallant, G. Gwinner, R. Klawitter, B. Kootte, A.A. Kwiatkowski, D. Lascar, K.G. Leach, A. Lennarz, E. Leistenschneider, D.A. Short, J. Dilling (C. Babcock, P. Reiter & Y. Lan not pictured) and the TITAN Collaboration

## Slide 50: July 2016: S1466 & S1502
10 days
Some of the cleanest beam from IGLIS
Measured masses of 18 states:
  125,125m,126,127,127mCd
  125,125m,126,126m,127,127mIn 128,128m,129,129mIn 130,130m1,130m2In
Will yield 2 pubs. min.
Chart: 125Cd
| 1
#REF! | -73348.1
#REF! | -73313.5699 | -73158.2536
#REF! | -73348.1 | -73162
#REF! | -73287
Chart: 126Cd
| 1
#REF! | -72256.8
#REF! | -72258.4587
#REF! | -72256.5 | -72266
Chart: 127Cd
| 1
#REF! | -68491
#REF! | -68707.2857 | -68444.7344
#REF! | -68493

## Slide 51: Gas stopper cell
Design of cryogenic gas catcher for the Super-FRS @ FAIR
From http://www.euroschoolonexoticbeams.be/site/files/2013_05_ExoBeams13_PThirolf_GasCell.pdf
RF carpet
Inner chamber at ~60-70K
Exit hole
Vacuum chamber for
Insulating vacuum
DC cage
electrodes
Degrader/
Entrance windows
He gas at 0.1-1bar
Ions
Gas stopper cells used at fragmentation facilities to stop RI-beams (GSI/FAIR, FRIB, RIKEN, KUL Leuven, CARIBU @ ANL, …)
Extraction efficiencies of >10% have been observed
Extraction times on the order of 10ms
Up to 103 ions/s space charge effects negligible; at higher ion intensities reduced transmission efficiency due to space-charge effects
Extreme pure gas required to reduce charge exchange and neutralization in the gas
RF-carpet of cryogenic stopper
EPL, 96 (2011) 52001
0.6mm
4 electrodes/mm
RF-funnel
For ion extraction
Slide courtesy of T. Brunner

## Slide 52: RF funnel concept
VRF = 120 V, f = 10 MHz
Simulated Ba+ transmission ~95%
RF-funnel concept for Ba-tagging:
Converging-diverging nozzle
2 Stacks total 301 electrodes
RF-field applied to electrodes
PA = 10 bar, PB = 1 mbar
VRF = 25V, f = 2.6 MHz
Simulated Ba+ transmission ~72%
Possible to extract ions from 10 bar Xe  initial design (and Ba-tagging design) by V. Varentsov for ion extraction from 0.1-1bar He
Optimization of design by V. Varetsov at GSI-FAIR
Extraction times O(10ms)
Int. J. Mass Spec. 379, 110 (2015)
RF carpet
To LPT
Stopper cell
Slide courtesy of T. Brunner

## Slide 53: MR-TOF-MS
Multi-reflection time-of-flight mass spectrometer based on Greifswald/ISOLDE design
Can be operated in beam cleaning mode (dm/m ~ 10-4) or mass-measurement mode (dm/m > 10-5)
Resolution limited by dispersion of MR TOF
IJMS 349 (2013) 123
Slide courtesy of T. Brunner

## Slide 54: Penning trap
Motion of ions well understood:
Three Eigenmotions can be coupled using RF
Allows us to manipulate motion:
transfer from one motion into the other
Cyclotron frequency:
Superposition of
strong magnetic field
weak electrostatic quadrupole field
kHz
MHz
dm/m > 10-7
Half lives below 10ms measured at TITAN
Notes: Talk about decoupling of eigenmotions
weakly mass dependent
strongly mass dependent
Talk about decoupling of eigenmotions
𝜈_− weakly mass dependent
𝜈_+ strongly mass dependent

## Slide 55: Status of EMMA Ion Optical Elements

## Slide 56: The rp-process
Waiting Points require nuclear masses
2p channel daughters have never been measured
  Example: 68Se(p,)(p,)70Kr
Specifically mentioned by rp-process theorists
  H. Schatz, IJMS, 349–350 1 (2013)
ISAC yields
72Kr: 440/s (measured)
70Kr: ~0.2/s extrapolated assuming yield reduction of 50/n
 Impossible to produce at ISAC
 Possible production at EMMA

## Slide 57: The rp-process case 70Kr
38K + 40Ca
200 MeV
Z
N
Rb
Kr
Br
Se
As
Ge
Ga
Zn
Cu
Ni
Co
70Kr
ISAC yields
72Kr: 440/s (measured)
70Kr: ~0.2/s extrapolated assuming yield reduction of 50/n
 Impossible to produce at ISAC
Possible production and separation at EMMA
Notes: 5.2 MeV/U

## Slide 58: The rp-process case 70Kr
35Ar + 40Ca
100 MeV
Z
N
Sr
Rb
Kr
Br
Se
As
Ge
Ga
ISAC yields
72Kr: 440/s (measured)
70Kr: ~0.2/s extrapolated assuming yield reduction of 50/n
 Impossible to produce at ISAC
Possible production and separation at EMMA
70Kr
Notes: 35Ar Production = /s with Ti target @ 70uA of proton current
70Kr cross section = 0.0457 mb
35Ar Production = 6.5×〖10〗^6/s with Ti target @ 70uA of proton current
70Kr cross section = 0.0457 mb

## Slide 59: Stellar reaction rates
Paper details a list of more than 1,000 nuclei that contribute to asymmetric reaction rates in:
Most are neutron-deficient
This is a goldmine of astrophysical motivation

## Slide 60: Nuclear structure – 100Sn
Two production mechanisms:
50Cr + 58Ni
  Chartier et al, PRL 77 12 (1996)
124/3Xe Fragmentation
  Hinke et al, Nature 486 7403 (2012)
N=Z
rp-process
Haloes –
Continuum Structure
Position of the dripline
Structural Changes
r-process path

## Slide 61: What is the pressure in MPET?
Slide courtesy of E. Leistenschneider
Notes: Particle in a cell simulation:
Individual particle tracking given system geometry
Collisions following Knudsen`s law
Material outgassing is main source of gas, others can also be included
"Calibrated" using actual measurements from IGs

## Slide 62: What pressure is required?
10-11 torr
  HCI
10-12 torr
  HCI
Slide courtesy of E. Leistenschneider

## Slide 63: Solution: Cryogenically cool the trap
Need to reduce pressure by factor of 300
Slide courtesy of E. Leistenschneider

## Slide 64: Cryocooler

## Slide 65: Rebuild/redesign the Penning trap
Notes: New electrodes to allow for cryopumping on the surface
RF to be applied at ring rather than guard/correction electrodes

## Slide 66: Transport System
Gas filled RFQ’s
  Carbon filled PPS rods for axial DC field
RFQ Switchyard
  Radial confinement through RF
  Axial control through DC gradient
Slide courtesy of P. Reiter
Notes: PPS = Polyphenylene Sulphide

## Slide 67: Analyzer
Based on AMBIPROBE @ JLU used for analytic mass spectrometry
  Two gridless, electrostatic ion mirrors
  Injection & ejections through pulsed endcaps
Slide courtesy of P. Reiter
Notes: PPS = Polyphenylene Sulphide

## Slide 68: Commissioning in mass separator mode
133Cs Charged Residual Air Particles from a hot cathode ion gauge
Slide courtesy of P. Reiter
Notes: C.R.A.P. = Charged Residual Air Particles

## Slide 69: Commissioning in mass separator mode
133Cs Charged Residual Air Particles from a hot cathode ion gauge
  Adjust retrapping time to capture Cs
Slide courtesy of P. Reiter
Notes: C.R.A.P. = Charged Residual Air Particles

## Slide 70: So we wait for a β-decay
The Sn where equilibrium occurs depends only on T and nn
[A. Champagne, RIA Summer School 06]
Some possible r-process paths
Stability
Notes: This process isn’t a single line. Many assumptions go into each model, even T and n_n have a range of possibilities
Note the path density at the closed shells.
N=50,82,126 → A=82,130,195

## Slide 71: Explosive nucleosynthesis
Fe Peak
Notes: Most A>56 nuclei produced in explosive processes.

## Slide 72: Neutron Separation Energy -
Preliminary
Notes: Sn is ugly because of odd-even pairing effects. Note the inversion when we switch from Cd and In. Because it’s ugly…

## Slide 73: (2)Neutron Separation Energy -
In
Z=49
Cd
Z=48
Preliminary
Notes: Here we see that in most cases calculated Sn our g.s. measurements agree with the AME values though in many cases we’re able to bring values town to the order of 10keV

## Slide 74: The TITAN MR-ToF
Standard MR-ToF isobar separator:
  Separation based on conversion of time in spatial spread by Bradbury-Nielsen Gate
Not possible due to space constraints
Novel MR-ToF Isobar Separator
  Separation based mass-selective retrapping
  Bunching, cooling & retrapping in the same trap
Compact system
Slide courtesy of P. Reiter

## Slide 75: Mass selective re-trapping
Slide courtesy of P. Reiter

## Slide 76: Analyzer performance – May 2016
Slide courtesy of D. Short
Goal Achieved
Notes: This is in mass measurement mode where the ions are sent to an MCP at the end of the analyzer.
To select masses, they have to be selectively retrapped for transport down the RFQ. Current best
This is in mass measurement mode where the ions are sent to an MCP at the end of the analyzer.
To select masses, they have to be selectively retrapped for transport down the RFQ. Current best 𝑅≈13𝑘

## Slide 77: Current
MR-ToF works for broad range of masses (Aug 2016)

## Slide 78: TITAN MR-TOF vs GSI MR-TOF
Comparison to the gold standard for MR-TOF’s with 133Cs
Notes:   GSI MR-TOF
    Larger analyzer  not a fair comparison
  Compare resolving power vs. Time-of-flight

## Slide 79: Commissioning in mass separator mode
R ~ 1.6 x 104 after 3.7 ms
Slide courtesy of P. Reiter
Notes: C.R.A.P. = Charged Residual Air Particles

## Slide 80: TITAN MR-TOF Re-Trapping
MCP
Detector
Ion mirror 1
Ion mirror 2
N = 129.5 turns
RF Ion Trap
MCP
Detector
Ion mirror 1
Ion mirror 2
N = 2 turns
1
2
Commissioning in mass separator mode
  1 ST 128.5 MT  separation power ~ 25.000 at 5V re-trapping potential
Slide courtesy of P. Reiter