## Slide 1
Detector Physics
Ionization Detectors
D. Lascar | Postdoctoral Fellow | TRIUMF
GAPS Postdoc Lecture Series – October 26, 2015

## Slide 2: Outline
Ionization Detectors
  Behavior in the detector
    Deposition of energy
    Transport within the detector
    Avalanche multiplication
  Detector Types
    Proportional counters
    Multiwire Proportional Counters (MWPCs)
    Gas Electron Multipliers (GEMs)
Limits

## Slide 3: Gas a detector medium
Gas is pretty cheap.
E deposited in the form of electron-ion pairs.
You can take advantage of electric fields to perform charge separation.
You can make the detector portable.
Sensitivity is improved with advances in electronics.
Notes: Bubble chambers and cloud chambers don’t count as ionization detectors. Also, they fell out of favor because they were primarily an optical medium => Advances in optical recognition software and digital photography could allow them to come back.

## Slide 4: Charged particle energy loss – Due to e-
Electrons don’t have much mass
Bragg peak
Range: The distance a particle travels in medium before coming to rest
Notes: Left – Energy loss in air as a function of particle KE
  Calculated via Bethe Bloch formula
  If density is in units of g/cm3 then E is in units of MeV
Right – 300 MeV proton in water
  If E-loss decreases with increasing energy, it increases with decreasing energy

## Slide 5: E loss due to e-: 2 types
Excitation X + p → X* + p
b at resonance
Dominates due to lower energy
No free electrons created
Excited ions can participate in subsequent ionizing reactions
Ionization X + p → X+ + p + e-
b
Higher energy threshold makes this less likely
What’s most important in gaseous detectors
Penning Effect: Ne* + Ar → Ne + Ar+ + e-

## Slide 6: Charged particles with molecules
PRIMARY IONIZATION: ELECTRON-ION PAIRS
Minimum ionizing particles:
Argon
DME
n
(ion pairs/
cm
)
25
55
dE/
dx
(
keV
/
cm
)
GAS (STP)
2.4
3.9
Xenon
6.7
44
CH
4
1.5
16
P
k
n
=
n
k
k
!
e
-
n
Statistics of primary ionization:
Poisson:
n: average
k: actual number
(Maximum) detection efficiency:
e
=
1
-
e
-
n
thickness

Argon
GAS (STP)
1
mm
91.8
2
mm
99.3
Helium
0.32
6
Helium
1
mm
45
2
mm
70
Slide courtesy of F. Sauli IEEE-NSS 2002
Notes: Eionization = 10-20 eV but what is required is typically 2x that.

## Slide 7: Secondary & total ionization
SECONDARY AND TOTAL IONIZATION
CLUSTERS & δ ELECTRONS:
Gas | Ionization Potential (eV) | (eV) | E-Loss (keV/cm) | N (cm-1)
Ar | 15.7 | 25 | 2,53 | 106
Xe | 12.1 | 22 | 6.87 | 312
He | 24.5 | 41.6 | 0.345 | 8.3
H2 | 15.6 | 36.4 | 0.32 | 8.8
N2 | 15.5 | 34.8 | 1.96 | 56.3
O2 | 12.5 | 30.2 | 2.26 | 74.8
CH4 | 12.6 | 30 | 1.61 | 54
C2H6 | 11.5 | 26 | 2.91 | 112
C4H10 | 10.6 | 26 | 5.67 | 220
CO2 | 13.8 | 34 | 3.35 | 100
Gas | Ionization Potential (eV) |  | E-Loss (keV/cm) | N (cm-1)
Ar | 15.7 | 25 | 2,53 | 106
Xe | 12.1 | 22 | 6.87 | 312
He | 24.5 | 41.6 | 0.345 | 8.3
H2 | 15.6 | 36.4 | 0.32 | 8.8
N2 | 15.5 | 34.8 | 1.96 | 56.3
O2 | 12.5 | 30.2 | 2.26 | 74.8
CH4 | 12.6 | 30 | 1.61 | 54
C2H6 | 11.5 | 26 | 2.91 | 112
C4H10 | 10.6 | 26 | 5.67 | 220
CO2 | 13.8 | 34 | 3.35 | 100
Statistical nature of ionization means W not strongly dependent on particle type or gas
Notes: Whenever an electron has enough energy to ionize another atom, the resultant free electrons are called secondary electrons or δ-electrons
Ionizing reactions are statistical in nature -> 2 identical particles won’t create the same number of E-I pairs
W = Mean energy/electron pair -> Not equal to Energy/ionization energy because excitation often happens

## Slide 8: DRIFT
ELECTRIC FIELD E = 0: THERMAL DIFFUSION
DRIFT AND DIFFUSION OF CHARGES IN GASES
ELECTRIC FIELD E > 0: CHARGE TRANSPORT AND DIFFUSION
E
IONS
ELECTRONS
Notes: Vt = thermal velocity
Without an E-field, the motion is a pure random walk.
With an E-field, the motion is interrupted by collisions but is overall in a single direction.

## Slide 9: Can we derive ?
Average time between collisions
Mean free path

## Slide 10: Mean free path - λ
Given a we can get – the Probability density function
  As long as the cumulative distribution function of is continuous.
From there, is just the expectation value of

## Slide 11: Can we derive ?
Electric field

## Slide 12: Can we derive ?
Ion Mobility
μ
Notes: This is for ions

## Slide 13: Can we derive ?
Given a drift field of 1 kV/cm:
Notes: This is for ions

## Slide 14: Gas mixture matters
Notes: This is for electrons
1 μm/ns = 1 km/s

## Slide 15: What is going on in the gas?
After recombination, Ar emits photon
  High prob. of e- from cathode
During recombination, collision with cathode likely emits more than 1 e-
Enough extra e- could cause a discharge
Chart: 
Ar
Metals
Notes: Ar first ionization potential is 11.6 eV

## Slide 16: What is going on in the gas?
After recombination, Ar emits photon
  High prob. of e- from cathode
During recombination, collision with cathode likely emits more than 1 e-
Enough extra e- could cause a discharge
Introduce polyatomic quenching gas (hydrocarbon).
  CH4 (Methane)
  C4H10 (Isobutane)
Many rotational & vibrational degrees of freedom
  Absorbs photons
  Charge exchange with Ar+ ions
Notes: When the quenching molecule reaches the cathode, charge exchange much less likely to emit secondary electrons.

## Slide 17: Ionization chamber
The most basic ionization detector.
Used for prompt radiation detection.
Low current: Given 1000 α/s and each track is
  19 fA
What happens when 1 e- is deposited?
ΔV
i
Notes: As voltage increases, the amount of electrons that make it to the anode approach 100%
Some smoke detectors measure ionization currents in air generated by Americium-241

## Slide 18: Challenge:
Single electrons are hard to detect. What to do?
Stronger Field
  Gives electrons more energy
  If the electrons have enough energy to ionize along their path
Constant E-field so avalanche everywhere
ΔV
i
PPAC
late
arallel
valanche
ounter
Notes: PPAC gives position sensitivity at the cost of charge/energy deposition knowledge
Ask where it would be useful. Onsite?
Before going to next slide, “So we have a medium where charge is deposited and a means of amplifying the charge, can we control it to get both position and energy?

## Slide 19: The Geiger-Müller tube
Cylinder filled with gas
Inner surface of the cylinder is conductive
If is applied to the wire:

## Slide 20: The Geiger-Müller tube
Drift Region
Multiplication Region

## Slide 21: The Geiger-Müller tube

## Slide 22: The Geiger-Müller tube
Notes: Go through each region as V0 increases.

## Slide 23: The Geiger-Müller tube
What you gain:
  Energy sensitivity that is scalable with voltage
  Position sensitivity in x or y
  Portability
What you lose:
  Position sensitivity in x and y or
  Money – get position back with an array.

## Slide 24: Proportional Tube Array
Photo courtesy of J.R. Hörandel http://particle.astro.ru.nl/etracersetup.html
Notes: You take advantage of the fact that the energy deposited in each tube won’t be 100%
This was part of the TRACER balloon project.
This layer had
  2 m long tubes.
  2 cm I.D.
  Walls made of aluminized mylar
Instrument made of 8 layers (4x and 4y)

## Slide 25: TRACER
Photo courtesy of J.R. Hörandel http://particle.astro.ru.nl/etracersetup.html
Photo courtesy of stratocat.com
Notes: More than 2000 tubes were built -> Labor intensive.
What if I don’t want to do this over a large area?

## Slide 26: TRACER
Photo courtesy of stratocat.com
Photo courtesy of stratocat.com
Notes: At the end of the flight the instrument detached from the balloon and parachuted to the ground
Upon landing, the instrument didn’t detach from the parachute so when the wind re-inflated the chute, the intrument was dragged for 6 miles

## Slide 27: Multiwire Proportional Chamber (MWPC)
What if you don’t want a plethora of independent gas volumes?
Each wire acts as its own proportional counter.
Could snake the wire and use a delay line.
Notes: Wires at V0. Cathodes are at Vc

## Slide 28: MWPC X-Y sensitivity
What if you want 2D sensitivity?
Create an array in X and an array in Y below.
Charge deposited above goes to the top array and
Signal induces an image charge on the opposite array

## Slide 29: E.G. The Time Projection Chamber (TPC)
If you know where and when an event starts, you have a trigger.
Most of the detector is a drift chamber.
Endcaps are MWPCs
determined via curvature in
Notes: Go through the diagram. Start with the structure. Note the magnetic field direction.

## Slide 30: TPC movie

## Slide 31: What if you need more gain?
It’s still hard to detect low energy events.
Proportional tubes/MWPCs have only one stage of charge multiplication.
Proportional tubes arrays & MWPCs are labor-intensive to assemble.
What is needed is an array of discreet charge multiplication regions.

## Slide 32: What is a GEM?
A Gas Electron Multiplier (GEM) is essentially a thin layer of kapton insulation sandwiched between two layers of copper.
Holes are then etched into the assembly.
A Gas Electron Multiplier (GEM) is essentially a thin layer of kapton insulation sandwiched between two layers of copper.
Holes are then etched into the assembly.
Many holes
A close-up of a single hole

## Slide 33: How does it work?
Behaves like a parallel plate capacitor.
e- channeled through holes
Fields in holes can reach ~120 kV/cm.
Charge multiplication inside the holes only.
GEMs can be stacked so multiplication can be done in stages

## Slide 34: Additional Material
The two textbooks
http://lhcb-muon.web.cern.ch/lhcb-muon/documents/Sauli_77-09.pdf
http://www.sciencedirect.com/science/article/pii/S0370157304003345#

## Slide 36: Consequences of E-loss statistics
CONSEQUENCES OF ENERGY LOSS STATISTICS
LANDAU DISTRIBUTION OF ENERGY LOSS:
For a Gaussian distribution:
sN ~ 21 i.p.
FWHM ~ 50 i.p.
0
0
500
1000
6000
4000
2000
N (i.p.)
Counts
4 cm Ar-CH4 (95-5)
5 bars
N = 460 i.p.
PARTICLE IDENTIFICATION
Requires statistical analysis of hundreds of samples
0
500
1000
6000
4000
2000
N (i.p)
Counts
0
protons
electrons
15 GeV/c
I. Lehraus et al, Phys. Scripta 23(1981)727
FWHM~250 i.p.
Slide courtesy of F. Sauli IEEE-NSS 2002